## Slide 1: Frequency Domain Filtering

## Slide 2: Spatial Domain
The spatial domain refers to the direct representation of a signal as it appears in its original form. In the context of images, each pixel's intensity values are directly related to the visual content.
Spatial domain operations involve manipulating pixel values directly. Typical operations include brightness/contrast adjustments, color transformations, edge detection, blurring, sharpening, and more.
The operations are usually simple and intuitive to understand, making them easy to implement and interpret.
Spatial domain operations might not always be efficient or suitable for complex transformations since they consider only local information and may not capture global patterns well.

## Slide 3: Frequency Domain
The frequency domain represents a signal in terms of its frequency components. It reveals the frequencies present in the signal and their respective magnitudes and phases.
In images and signals, frequencies correspond to patterns such as textures, edges, and overall structures. Low-frequency components capture gradual changes, while high-frequency components represent rapid changes.
Frequency domain transformations involve converting a signal from its spatial representation to its frequency representation using techniques like the Discrete Fourier Transform (DFT) or Fast Fourier Transform (FFT).
Frequency domain operations include filtering, noise removal, compression, and feature extraction.
Frequency domain operations are often powerful for analyzing and processing signals but might require some understanding of signal processing concepts.

## Slide 4: Frequency Domain Filters
Frequency domain filters are used in signal and image processing to manipulate the frequency components of a signal in the frequency domain.
These filters are applied to the Fourier-transformed representation of the signal to modify its frequency content, and then the inverse Fourier transform is performed to bring the signal back to the spatial domain.
Frequency domain filters are particularly useful for tasks like noise reduction, sharpening, blurring, and edge detection.

## Slide 5: Low-Pass Filters
Low-pass filters allow low-frequency components (such as smooth changes and global patterns) to pass through while attenuating high-frequency components (such as noise and fine details).
Ideal Low-Pass Filter: This filter completely removes high-frequency components beyond a certain cutoff frequency.
Gaussian Low-Pass Filter: This filter attenuates higher frequencies smoothly with a Gaussian-shaped roll-off.
Butterworth Low-Pass Filter: This filter provides a more gradual roll-off than the ideal filter.

## Slide 6: High-Pass Filters
High-pass filters allow high-frequency components (such as edges and fine details) to pass through while attenuating low-frequency components (such as uniform regions).
Ideal High-Pass Filter: This filter removes low-frequency components below a specified cutoff frequency.
Gaussian High-Pass Filter: Similar to the Gaussian low-pass filter, but attenuates lower frequencies.

## Slide 7: Band-Pass Filters
Band-pass filters allow a range of frequencies within a certain band to pass through while attenuating frequencies outside that band.
They are useful for isolating specific frequency components of interest while removing unwanted frequencies.

## Slide 8: Notch Filters
Notch filters are used to attenuate or remove specific frequencies from a signal.
They are particularly useful for removing specific types of noise or interference.

## Slide 9: Homomorphic Filters
Homomorphic filters are used to enhance the details of an image while correcting for non-uniform lighting conditions.
They can be used to improve the visibility of details in images with varying illumination.

## Slide 10: Wiener Filters
Wiener filters are used for signal deconvolution and noise reduction.
They aim to minimize the mean square error between the original signal and the estimated signal.

## Slide 11: How to Apply?
Applying frequency domain filters involves the following steps:
Perform the Discrete Fourier Transform (DFT) on the signal.
Apply the filter in the frequency domain by modifying the Fourier coefficients.
Perform the Inverse Discrete Fourier Transform (IDFT) to bring the filtered signal back to the spatial domain.