## Slide 1: COA
Types of Machine Instructions

## Slide 2: Types of Machine Instructions
Data Transfer Instructions
Data Manipulation Instructions
Program Control Instructions

## Slide 3: Data Transfer Instructions
LOAD: Data transfers from memory to register
STORE: Data transfers from register to memory
MOVE: Data transfers from register to register
IN: Transfers data from input devices to register
OUT: Transfers data from register to output device.
PUSH: Gets data from memory or register on to the top of stack
POP: Gets data from top of the stack to memory or register
XCHG: Exchanges the data between memory and registers

## Slide 4: Data Manipulation Instructions
Arithmetic Instructions: ADD, SUB, MUL, DIV, INC, DEC, etc.
Logical Instructions: AND, OR, EXCLUSIVE-OR, NOT, shift, rotate, etc.
Arithmetic and Logical Instructions: SAL, SAR, etc.

## Slide 5: Program Control Instructions
Compare and Test Instructions: To compare and test status flags condition code register is required.
  Conditional code register (CCR):
    5 status bits:
      Carry borrow (C)
      Overflow (V)
      Zero (Z)
      Negative (N)
      Half Carry (H)
    2 interrupt masking bits
    1 stop disable bit