## Slide 1: Cache Memory Management
Direct Mapped Cache
Fully Associative Cache
Set Associative Cache

## Slide 2: GATE 2017
A cache memory unit with capacity of N words and block size of B words is to be designed. If it is designed as direct mapped cache, the length of the TAG field is 10 bits. If the cache unit is now designed as a 16-way set-associative cache, the length of the TAG field is ______ bits.
A. 12
B. 14
C. 16
D. 18

## Slide 3: Answer: (B)

## Slide 4: Question (GATE 2021)
Consider a set-associative cache of size 2KB (1KB=210 bytes) with cache block size of 64 bytes. Assume that the cache is byte-addressable and a 32 -bit address is used for accessing the cache. If the width of the tag field is 22 bits, the associativity of the cache is _________ .
(A) 2
(B) 4
(C) 1
(D) 8

## Slide 5: Answer: A

## Slide 6: GATE 2007
Consider a 4-way set associative cache consisting of 128 lines with a line size of 64 words. The CPU generates a 20-bit address of a word in main memory. The number of bits in the TAG, LINE and WORD fields are respectively:
(A) 9,6,5
(B) 7, 7, 6
(C) 7, 5, 8
(D) 9, 5, 6

## Slide 7: Answer: D

## Slide 8: GATE 2008
Consider a computer with a 4-ways set-associative mapped cache of the following characteristics: a total of 1 MB of main memory, a word size of 1 byte, a block size of 128 words and a cache size of 8 KB.
The number of bits in the TAG, SET and WORD fields, respectively are:
(A) 7, 6, 7
(B) 8, 5, 7
(C) 8, 6, 6
(D) 9, 4, 7

## Slide 9: Answer: D

## Slide 10: Question
A 4-way set-associative cache memory unit with a capacity of 16 KB is built using a block size of 8 words. The word length is 32 bits. The size of the physical address space is 4 GB. The number of bits for the TAG field is _____
(A) 5
(B) 15
(C) 20
(D) 25

## Slide 11: Answer: C

## Slide 12: GATE 2016
The width of the physical address on a machine is 40 bits. The width of the tag field in a 512 KB 8-way set associative cache is ____________ bits Ans.D
(A) 24
(B) 20
(C) 30
(D) 40

## Slide 13: RISC and CISC

## Slide 14: Reduced Instruction Set Architecture (RISC)
The main idea behind this is to make hardware simpler by using an instruction set composed of a few basic steps for loading, evaluating, and storing operations just like a load command will load data, a store command will store the data.
RISC: Reduce the cycles per instruction at the cost of the number of instructions per program.

## Slide 15: Complex Instruction Set Architecture (CISC)
The main idea is that a single instruction will do all loading, evaluating, and storing operations just like a multiplication command will do stuff like loading data, evaluating, and storing it, hence it’s complex.
Both approaches try to increase the CPU performance
CISC: The CISC approach attempts to minimize the number of instructions per program but at the cost of an increase in the number of cycles per instruction.

## Slide 17: Characteristic of RISC
Simpler instruction, hence simple instruction decoding.
Instruction comes undersize of one word.
Instruction takes a single clock cycle to get executed.
More general-purpose registers.
Simple Addressing Modes.
Fewer Data types.
A pipeline can be achieved.

## Slide 18: Characteristic of CISC
Complex instruction, hence complex instruction decoding.
Instructions are larger than one-word size.
Instruction may take more than a single clock cycle to get executed.
Less number of general-purpose registers as operations get performed in memory itself.
Complex Addressing Modes.
More Data types.

## Slide 19
RISC | CISC
Focus on software | Focus on hardware
Uses only Hardwired control unit | Uses both hardwired and microprogrammed control unit
Transistors are used for more registers | Transistors are used for storing complex Instructions
Fixed sized instructions | Variable sized instructions
Can perform only Register to Register Arithmetic operations | Can perform REG to REG or REG to MEM or MEM to MEM
Requires more number of registers | Requires less number of registers
Code size is large | Code size is small
An instruction executed in a single clock cycle | Instruction takes more than one clock cycle
An instruction fit in one word | Instructions are larger than the size of one word

## Slide 20: What is Pipelining
Pipelining is accumulating the instructions from the processor through a pipeline or a data pipeline. A Pipeline is a set of data processing units arranged in series such that the output of one element is the input of the subsequent element. Pipelining is a technique in which multiple instructions are overlapped during execution. It is used primarily to create and organize instructions in a processor so that the processes run in concurrent fashion. Basically, Pipelining is a process to manage the addition of new tasks frequently by removing the completed tasks.

## Slide 21: Difference between Pipelining and Non-Pipelining
Pipelining System | Non-Pipelining System
In pipelining system, multiple instructions are overlapped during execution. | In a Non-Pipelining system, processes like decoding, fetching, execution and writing memory are merged into a single unit or a single step.
Many instructions are executed at the same time | Only one instruction is executed at the same time
The efficiency of the pipelining system depends upon the effectiveness of CPU scheduler. | In a Non-Pipelining system, The CPU scheduler chooses the instruction from the pool of waiting instructions, when an execution unit gives a signal that it is free. The efficiency is not dependent on the CPU scheduler.
Execution time is comparatively less and execution is done in a fewer cycles | Execution takes more time or more number of cycles comparatively

## Slide 22: Question: GATE2000

## Slide 23: Answer: B

## Slide 24: Question (GATE2009)
Consider a 4 stage pipeline processor. The number of cycles needed by the four instructions I1, I2, I3, I4 in stages S1, S2, S3, S4 is shown below:
What is the number of cycles needed to execute the following loop?
for (i=1 to 2) { I1; I2; I3; I4; }
A. 16 B. 23
C. 28 D. 30

## Slide 25: Answer: B